SNS Work Planning Checklist

It is the author's responsibility to research and understand each of these questions with respect to the scope of the work they are planning. The author should involve Subject Matter Experts (SMEs) that may be needed to make sure that a safe working environment is established and maintained are involved, as appropriate, in the planning and execution of the work. SMEs may be identified on the work plan as a reviewer.

Questions 1-4 apply to the Job Level.  Use the resources and guidelines available when clicking on each question to determine the appropriate Job Grade for this work.

Questions 5-29 apply to various aspects of the work to be performed.  Review the resources and guidelines by clicking on each question number.  Apply the appropriate actions to either the Prerequisites/Precautions, Directions, Post Work Testing, or Closeout entry fields.

Determine the appropriate Job Level 1. Will this work effect the operations of a Credited Control Level 1: Credited Controls Work that involves changes to a Credited Control. Description Change or Modification of a Credited Control 2. Will this work effect, or have a potential negative impact on, Credited Controls or Life Safety Equipment or result in significant modifications to primary facility Structures, Systems or Components? Can this work adversely impact operational availability? Level 2: Life Safety, High Rigor Equipment, Facility Modifications, Facility Impact Life Safety Functional features relative to fire, storm, collapse, crowd behavior, and other related safety considerations within a structure or facility. Credited Controls Equipment Credited Control Maintenance, repair, calibration, troubleshooting/testing, or authorized replacement Facility Modifications Credited Controls Related Facility Modification Non-Credited Controls Related Major Facility Modification Significant changes to facilities that are governed by Building, Fire, or other recognized codes or standards. Facility Impact Changes to the Facility that could adversely impact facility operation (mission availability). 3. Will this work follow an Operations Procedure, Internal Operating Procedure or Pre-Approved Work Plan? Will this work require job-specific permitting for personnel safety, such as for energized electrical work requiring an approved Job Hazard Analysis (JHA) or require a special permit, or require a high level of coordination due to the fact that the work might have a significant impact on laboratory operations? Level 3 Work activities not classified as Grade 1 or 2 that require job specific permitting for personnel safety, or a high level of coordination due to the fact that the work might have a significant impact on laboratory operations. This work will follow written, approved work planning documentation including, but not limited to Operations Procedures Manual (OPM) or Internal Operating Procedures (IOP) or Work Plan. 4. Can this work be planned and safely performed by the workers without direct field supervision? Level 4 Tasks that can be planned safely performed by empowering workers to utilize their skill level and technical capabilities without direct field supervision.

Special regulatory considerations

Does this work have the potential to impact other systems? 5. Will this work have a potential to impact the operation of Life Safety systems (alarms, egress, sprinklers)? Actions If a utility outage or other planned maintenance activity will affect fire protections systems or other life safety systems, then the task leader shall include a prerequisite to notify an ORNL Fire Protection Engineer for compensatory actions. A phone call to 574-5678 (Fire Department) does NOT initiate action on the fire protection engineers behalf and is not an acceptable alternative. Work which obstructs emergency exit pathways shall be evaluated to ensure egress alternatives are available and the amount of time the normal egress block is minimized. Add step(s) in Directions section to provide supplemental fire protection. Combustibles introduced into buildings should be limited. If work requires combustibles to remain in buildings for extended periods of time, Fire Protection Engineering should be consulted to develop compensatory measures. If work will generate dust, smoke, or fumes which could set off smoke detectors, then Fire Protection Engineering should be consulted for compensatory actions. Add step in Directions section for QA to witness penetration sealing. Work which obstructs emergency exit pathways shall be evaluated to ensure egress alternatives are available and the amount of time the normal egress block is minimized. Resources Fire Protection Engineering

Does this work have the potential to impact other operations? 6. Will work shut down systems which could affect other facility operations? Actions Add Prerequisite to notify Facility Management or Operations Manager of work activity. Plan/schedule work with Facility Management or Operations Manager. 7. Will this work require the facility to be placed in certain operating conditions, e.g. Facility Shutdown? Actions Consult Facility Management to determine facility operating conditions. Identify in Scope/Discussion section any need for configurations as work evolutions require. Provide system requirements and plant status requirements.

Will this work require special administrative control? 8. Will the project require excavations or penetrations? Actions Complete applicable SNS Excavation Permit or Penetration Permit Comply with excavation/penetration process as defined in the Subject Area Excavation/Penetration Contact EPO/ECR Penetrations typically involving removing or displacing material from a facility structure. Examples including: drilling or core drilling >2 inches deep into concrete wall, floor slabs, or roof slabs concrete cutting to remove sections of a concrete wall, floor, or roof drilling holes into building structural members (wood, timber, steel, or concrete columns, beams, joists, etc.) removing building structural members OR Excavations typically involving the movement, placement or removal of soil, rock, or other structures below the surface of the ground. Examples include: auguring, backfilling, digging, ditching, drilling, grading, plowing-in, pulling-in, ripping, scraping, trenching and tunneling removing soil or rock below grade removing an underground building foundation (footer, grade beam, caisson, etc.) removing an underground utility structure (manhole, headwall, pipe, etc.) drilling a well (for water or environmental sampling) geotechnical push probe penetration into soils driving fence post(s) >12 inches deep driving piles all trenchless pipe installation technology including pipe bursting, pipe ramming (including slick bore), directional boring, etc. Resources Excavation/Penetration Permit Exclusions Penetrations Less Than 2 " Work Requirements Excavation/Penetration 9. Will administrative tagging for configuration control/status be needed? Actions Add step for appropriate administrative tagging, i.e., LO/TO, Radiation Safety Holds. Resources Hazard Identification Signs and Tags Operations Manager Facility Management SNS Lockout/Tagout of Hazardous Energy Sources

Are there any special quality considerations? 10. Will the work require quality assurance hold points for inspection and verification? Actions Add step in Directions section to identify those points in which QA inspection is required. Resources Controlled Manufacturing Plan (e.g. ASME code work) 11. Will the work require post-work testing (Mandatory for Credited Controls related systems)? Actions Add step to Closeout section for Facility Management or Operations Management and task leader performance of post-work testing. Determine if post-work testing is required. Use surveillance test procedures as appropriate. Determine post-work testing requirements and acceptance criteria. Resources Facility Operations Basis Quality Vendor manuals 12. Does the work require task-specific training or qualification? Actions Add step to Prerequisite section to identify type of special training and who is required to attend. Include training records in work package/plan. Resources Training Requirements Matrix Facility Management 13. Do you know of history/lessons learned that could benefit this work? Actions Add step on Prerequisites section to review Lessons Learned/operating experience. Incorporate Lessons Learned in Directions section. Resources ORNL Lessons Learned Program Facility Management 14. Will drawings or vendor manuals be needed to do the work? Actions Add steps to Directions section as specified by drawings. Add steps to Directions section to reference vendor manuals. If work requires major disassembly/reassembly and would benefit from component labeling to complete the work correctly, then steps and/or tables should be added to the work instructions to ensure labeling and documentation. For example, rewiring of a control panel may involve wire labeling and a table in the work package/plan that documents correct wire reconnection. Include appropriate sections of vendor manual in package/plan. Insert any useful drawings in work package/plan. Verify current versions of drawings are being used. Resources Operations Manager Facility Management 15. Will calibrated measuring and test equipment be needed to do the work? Actions If work is to be performed on Credited Controls equipment, the task leader shall determine the need for calibration verification (such as a single-point check in the range to be used) of the M&TE to be used. Record instrument number and calibration date in work package/plan. Verify M&TE calibration is current. Resources Facility Management Calibration 16. Will the work require special controls for procurement of materials or services (e.g. for Level 1 and 2)? Actions Add steps in the Closeout section to return unused material for proper storage and inventory control. Determine procurement requirements for materials or parts. For Credited Controls equipment, the task leader should obtain material or parts in accordance with applicable procurement requirements. Include documentation in work package/plan which provides traceability of the material used. Documentation is required for safety-related materials. Examples include dedication package cover sheet, material issue form, and the receipt inspection report. Include in package/plan any special storage requirements needed during work package/plan execution in the Directions section. Resources Purchasing Supplies and Services

ES&H Compliance 17. Are there specific Resource Conservation/Pollution Prevent/Waste Minimization options for this project? Actions Plan, conduct, and close out work activities to reduce or eliminate waste and reduce costs. Resources Waste Minimization and Pollution Prevention SNS Waste Minimization 18. Will this activity involve work in radiological areas, the use of radioactive materials or Radiation Generating Devices or could this work affect the radiological control conditions of an approved Radiological Design Review or Radiological Work Review? Actions Obtain Radiological Support Services staff review of applicable design packages, work packages or work plans. Design install, and operate in a manner to safely control radioactive materials or radiation emissions. Ensure any changes in radiological material inventory are permissible under the facility inventory limitations identified in the Facility Use Agreement and are incorporated into the facility's radiological material inventory tracking for facility hazard categorization Resources Radiological Work: Performing Work Radiological Work: Preparing for Work Determining Facility or On-site Transportation Activity Hazard Category Radiological Design Requirements Radiation Generating Devices