SNS Typical Hazards to Be Found in a Job Hazards Analysis/Evaluation

Typical Hazards to be Considered in Job Hazard Evaluation

Work Plan Name: Work Plan Author: Work Scope Description: Date:

Hazards Requiring Permits / Special Authorization Resources Potential Controls (may not be all-inclusive) Asbestos/Man-Made Mineral Fibers Asbestos Management Program Asbestos UCN-13385, Asbestos Work Authorization and Disposal Request Beryllium OSSD Rep Working with Beryllium Beryllium Protection Program Elements (address in operation-specific work plan) Exposure monitoring Reduction and minimization of exposures Protective clothing and equipment Hygiene facilities and practices Housekeeping Medical surveillance Training Warning signs and labels Waste disposal Beryllium emergencies Recordkeeping Performance feedback Confined Space DSO/OSSD Rep. Confined Space Confined Space Program Manager Confined Space Entry Permit De-energized Hazardous Energy Sources Lockout/Tagout of Hazardous Energy Sources Lockout/Tagout Permit Electrical high voltage (>600v) Interface with Subcontractors when Overtagging of High Voltage (600V+) Systems Power Distribution Work Permit Energized Electrical (>50v) Energized Work, Performing: Interim Procedure JHA Permit Excavation/penetration (includes trenching and shoring) DSO/OSSD Rep. Excavation/Penetration Managing Excavated Soil Barriers for trenches Buddy Watch (best management practice only, must select additional controls) Covers for open pits Hard Hats Physical personnel barriers Signs or Markings ORNL Excavation Permit ORNL Penetration Permit Fissionable Material ORNL Nuclear Criticality Safety (NCS) Staff ORNL NCS Program ORNL Nuclear Criticality Safety (NCS) Staff Nuclear Criticality Safety Approval (NCSA) Hoisting and Rigging DSO/OSSD Rep. Hoisting and Rigging Preparing for Hoisting and Rigging Activities Critical Lift Plan Hard Hats Ordinary Production Lift Plan Pre-engineered Production Lift Plan Qualified personnel Safety shoes Traffic control Lead OSSD Rep Lead Program Manager (Subject Matter Expert) Working with Lead Lead Compliance Plan (consult with Lead Program Manager to determine need) Location of the project Description of the project activity Engineering controls Work Practice controls Respiratory protection Protective clothing Site-specific hazards and control methodology Exposure assessment Administrative controls Medical surveillance and biological monitoring schedule Training Information and notification Implementation schedule Contractor arrangements Radiological Work Radiological Support Services Radiological Work: Performing Work Radiological Work: Preparing for Work Radiological Work Permit (Enter RWP No.) Welding/burning/hot work Welding, Burning, and Hot Work DSO/OSSD Rep. Welding/Burning/Hot Work Permit Physical Hazards Resources Potential Controls (may not be all-inclusive) Atmospheric Issues - Oxygen enriched/Oxygen deficient DSO/OSSD Rep. Fire Protection Engineers Fire Protection, Prevention, and Control Preventing Fires and Controlling Fire Hazards Atmospheric monitoring Non-sparking tools and equipment Respiratory protection (Specify) Ventilation Boiler, Pressure Vessels, Relief Valves Pressure Vessels and Related Components Design to ASME code Inspection of vessels Labeling or other markings Compressed Gas DSO/OSSD Rep. Compressed Gas Cylinders and Related Systems Regular inspection (flammable or toxic gases) Rotation of stock Secondary containment Securing of cylinders Segregation of incompatible gases Transportation of cylinders controls Cryogenics Chemical Safety DSO/OSSD Rep. Recognized Industrial Practices for Activities Involving the Storage, Handling and Use of Hazardous Chemicals Engineering controls Face shields Gloves (Specify) Guard against air (oxygen) collection in cryogenic reservoirs Refill liquid when below a specified level Special valving Elevated Work DSO/OSSD Rep. Ladders Walking/Working Surfaces and Fall Protection Buddy system (best management practice only, must select additional controls) Ladder inspection Man lifts Safety harness/Fall protection equipment Scaffold Work platform Safety Monitoring System (Special Roofing Work Only) Ergonomic Conditions (Contact Stress, Vibration, Posture, Force, Repetitive Motion) DSO/OSSD Rep. Ergonomics Guidelines for Ergonomic Hazard Prevention and Control Diversify activities Evaluation of work station or Evaluation of work posture/positioning PPE (Specify) Stretch breaks/exercises Worker rotation Special Tools (Lifts, etc.) Explosives/Shock Sensitive Chemical Safety DSO/OSSD Rep. Explosives Spill Response and Discovery of Shock Sensitive Materials Face, eye, hand and torso protection Shields Special storage requirements Special waste provisions Usage plan Flammables Storing and Handling Flammable and Combustible Liquids Using Hazardous Chemicals Approved storage units Compatibility of flammable compounds Fire extinguisher Grounding for transfers Heat/Cold Stress DSO/OSSD Rep. Evaluating Temperature Extremes Guidelines for Thermal Stress Heat Stress Training Acclimatization Cool suits/cool vests Environmental/Physiological monitoring Frequent breaks PPE prescribed by OSSD (Specify) Work/rest regimen (Specify) Worker rotation Lasers Lasers Engineered and Administrative Control Matrix Laser Eye Protection Eye protection Inspections Interlocks Barriers/Curtains/Beam Stops Laser Training Low Power Laser Hazard Awareness Training High Power Laser Safety Training Low Clearance DSO/OSSD Rep. Engineering controls (guards) Signs or other markings Magnets DSO/OSSD Rep. Signs or other markings Manual Lifting DSO/OSSD Rep. Ergonomics Guidelines for Ergonomic Hazard Prevention and Control 2-person lift Diversity of activities Lifting Aides Proper lifting techniques Noise DSO/OSSD Rep. Hearing Conservation Dampering Engineering Controls Hearing protection (plugs or muffs) Medical testing Workplace monitoring Non Ionizing Radiation Radiological Support Services DSO/OSSD Rep. Signs or other markings Obstructed Access/Egress Building Safety Codes Facility Management Life Safety Code: NFPA 101 Alternative exits Signs or Markings Power Equipment OSSD Rep Hoisting and Rigging Preparing for Hoisting and Rigging Activities Cages Hearing protection PPE (Specify) Physical protection (roll bars) Qualified operator Seat belts Thermal Sources DSO/OSSD Rep. Signs or other markings Unguarded Equipment DSO/OSSD Rep. Machine Guarding Add guarding Other physical barriers Signs or markings Chemical Hazards Resources Potential Controls (may not be all-inclusive) Chemical or Product Name Chemical Safety MSDS F&O Approved Chemical List Acid suits Administrative controls Aprons Chemical goggles Engineering controls Eyewash/safety shower Face shields Gloves (Specify) Goggles Job Specific Haz Com Training Lab coats Medical monitoring Suitable shoes Ventilation Workplace monitoring Respirator Safety Glasses Training Hazardous Waste Hazardous and Mixed Waste Management MSDS F&O-ADM-012, Chemical Procurement and Management Chemical substitutions PPE (Specify) Workplace monitoring Biological Hazards Resources Potential Controls (may not be all-inclusive) Cooling tower and Legionella DSO/OSSD Rep. Biohazards Biohazard SME Fall protection Medical monitoring Respiratory protection (Specify) Infectious materials DSO/OSSD Rep. Working with Blood Borne Pathogens Derived from Humans Control plan Immunization PPE (Specify) Qualified personnel Insects/animals/wildlife/parasites DSO/OSSD Rep. Insect spray PPE (Specify) Snake guards Other Hazards Resources Potential Controls (may not be all-inclusive) Other Hazards (1) (Specify) Additional Controls (Specify) Other Hazards (2) (Specify) Additional Controls (Specify) Other Hazards (3) (Specify) Additional Controls (Specify) Other Hazards (4) (Specify) Additional Controls (Specify)